## Slide 1: Multi-layer object initialization in GPU_MS
Yi Jiang
06/02/2021

## Slide 2: Workflow & Parameters
Steps | Parameters
Load previous multi-layer object in p | p. model_object = false; p. model.object_type = 'rand'; initial_iterate_object_file{1} = preReconPosFile; p. multiple_layers_obj = true; % load multi-layers object
Select layers | eng. init_layer_select = [];
Pre-process (selected) layers | eng. init_layer_preprocess = ''; % '' or 'all' (default): use all layers (do nothing) % 'avg': average all layers % ‘avg1’: keep only one averaged layer % 'interp': interpolate layers eng. init_layer_interp = []; % desired depths if using ‘interp’
Add more layers | eng. init_layer_append_mode = ''; % '' or 'vac' (default): add vacuum layers % 'edge': append 1st or last layers % 'avg': append averaged layer
Rescale layers | eng. init_layer_scaling_factor = 1;

## Slide 3
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
eng.init_layer_select = [];
eng.init_layer_preprocess = ‘’;
eng.init_layer_append_mode = ‘vac’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;
Add vacuum layers
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm

## Slide 4
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
Add first or last layers
eng.init_layer_select = [];
eng.init_layer_preprocess = ‘’;
eng.init_layer_append_mode = ‘edge’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;

## Slide 5
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
Use one layer
eng.init_layer_select = [3];
eng.init_layer_preprocess = ‘’;
eng.init_layer_append_mode = ‘edge’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;

## Slide 6
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
Use three layers
eng.init_layer_select = [2:4];
eng.init_layer_preprocess = ‘’;
eng.init_layer_append_mode = ‘edge’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;

## Slide 7
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
Use the average of three layers
eng.init_layer_select = [2:4];
eng.init_layer_preprocess = ‘avg’;
eng.init_layer_append_mode = ‘edge’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;

## Slide 8
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
Use the average of three layers + add air layers
eng.init_layer_select = [2:4];
eng.init_layer_preprocess = ‘avg’;
eng.init_layer_append_mode = ‘vac’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;

## Slide 9
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 7
dz = 8 μm
Total thickness = 56 μm
Use the average of three layers + add air layers
eng.init_layer_select = [2:4];
eng.init_layer_preprocess = ‘avg1’;
eng.init_layer_append_mode = ‘vac’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 1;

## Slide 10
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 10
dz = 4 μm
Total thickness = 40 μm
Use the average of three layers to initialize layers w. different dz
eng.init_layer_select = [2:4];
eng.init_layer_preprocess = ‘avg’;
eng.init_layer_append_mode = ‘edge’;
eng.init_layer_interp = [];
eng.init_layer_scaling_factor = 0.5;

## Slide 11
Input object file:
Nlayers = 5
dz = 8 μm
Total thickness = 40 μm
Initial object for reconstruction:
Nlayers = 10
dz = 4 μm
Total thickness = 40 μm
Double the # of layers via interpolation
eng.init_layer_select = [];
eng.init_layer_preprocess = ‘interp’;
eng.init_layer_append_mode = ‘’;
eng.init_layer_interp = [1:0.5:5.5];
eng.init_layer_scaling_factor = 0.5;
1
2
3
4
5
1
2
3
4
5
1.5
2.5
3.5
4.5
5.5